## Slide 1
Developing Experts All rights reserved © 2021
KS4-17-09: Using Resources - Explore water safe to drink
● Describe the difference between potable and pure water
● Describe the steps used to produce potable water from fresh water and from salty water
Key Facts:
Water of appropriate quality is essential for life. For humans, drinking water should have sufficiently low levels of dissolved salts and microbes. Water that is safe to drink is called potable water. Potable water is not pure water in the chemical sense because it contains dissolved substances.
The methods used to produce potable water depend on available supplies of water and local conditions.
In the UK, rain provides water with low levels of dissolved substances (fresh water) that collects in the ground, in lakes, and rivers, and most potable water is produced by:
choosing an appropriate source of fresh water
passing the water through filter beds
sterilising
Sterilising agents used for potable water include chlorine, ozone or ultra-violet light.
If supplies of fresh water are limited, desalination of salty water or sea water may be required. Desalination can be done by distillation or by processes that use membranes such as reverse osmosis. These processes require large amounts of energy.
Potable water is water that has been processed and is safe for human consumption and daily use.
The difference between pure water and potable water is that pure water is solely made up of H2O molecules, whereas potable water may contain different substances, usually dissolved minerals and salts.
Potable water should have the following characteristics:
  Have a pH between 6.5 and 8.5.
  The dissolved substances (e.g. salt) will be within a normal range i.e. not saturated.
  Be free of bacteria or potentially harmful microbes.
Water is considered fresh when it is relatively free from dissolves substances e.g. rainwater.
Water can collect in reservoirs, lakes and rivers and is known as surface water.
In addition, it can collect in aquifers which are rocks that collect water underground.
This water is called groundwater.
Did you know…
We're one of the UK's largest water and wastewater services company. Every day we supply around 2.6 billion litres of drinking water to nine million customers. We also remove and treat 4.4 billion litres of sewage every day for 15 million customers.
The difference between distillation and desalination is distillation is the action of separating a solution by heating or cooling and desalination is the removal of salt from salt water. That is the difference between distillation and desalination.

## Slide 2
Developing Experts All rights reserved © 2021
KS4-17-09: Using Resources - Explore water safe to drink
● Describe the difference between potable and pure water
● Describe the steps used to produce potable water from fresh water and from salty water
Define the terms:
Potable water: ______________________________________________________________________________________________________________________________________________________________________
Pure water:
______________________________________________________________________________________________________________________________________________________________________
Explain the differences between the two terms.
Extended writing: describe the process of desalination.
Extended writing: describe the process of distillation
Extended writing: explain why distillation separates substances.
Grade 9: explain what happens to substances during the process of distillation in terms of intermolecular forces of attraction.
Desalination
Desalination is the removal of salt from seawater. This produces clean drinking water and is particularly useful in countries that have coastlines but no readily available fresh water sources, such as rivers and streams.
Desalination uses one of two main methods. The first is reverse osmosis, where seawater is forced through a membrane at high pressure. The membrane
allows water molecules to pass through but prevents
any other chemicals dissolved in the water from
passing through.
The second is thermal desalination. Older (thermal)
desalination plants may work using a principle similar
to distillation:
the salt water is heated or the water is allowed
to evaporate
the water vapour is collected rather than being
lost
the water vapour is condensed to form pure
water/fresh water
the salt is left behind and can be used for other
purposes
Distillation
Simple distillation is used to separate a solvent from a solution. It is useful for producing pure water from seawater.
Simple distillation works because the dissolved solute has a much higher boiling point than the solvent. When the solution is heated, solvent vapour leaves the solution. It moves away and is cooled and condensed. The remaining solution becomes more concentrated as the amount of solvent in it decreases.

## Slide 3
Developing Experts All rights reserved © 2021
KS4-17-09: Using Resources - Explore water safe to drink
● Describe the difference between potable and pure water
● Describe the steps used to produce potable water from fresh water and from salty water
Define the terms:
Potable water: ______________________________________________________________________________________________________________________________________________________________________
Pure water:
______________________________________________________________________________________________________________________________________________________________________
Explain the differences between the two terms.
______________________________________________________________________________________________________________________________________________________________________
______________________________________________________________________________________________________________________________________________________________________
______________________________________________________________________________________________________________________________________________________________________
______________________________________________________________________________________________________________________________________________________________________
Desalination
Desalination is the removal of salt from seawater. This produces clean drinking water and is particularly useful in countries that have coastlines but no readily available fresh water sources, such as rivers and streams.
Desalination uses one of two main methods. The first is reverse osmosis, where seawater is forced through a membrane at high pressure. The membrane
allows water molecules to pass through but prevents
any other chemicals dissolved in the water from
passing through.
The second is thermal desalination. Older (thermal)
desalination plants may work using a principle similar
to distillation:
the salt water is heated or the water is allowed
to evaporate
the water vapour is collected rather than being
lost
the water vapour is condensed to form pure
water/fresh water
the salt is left behind and can be used for other
purposes
Distillation
Simple distillation is used to separate a solvent from a solution. It is useful for producing pure water from seawater.
Simple distillation works because the dissolved solute has a much higher boiling point than the solvent. When the solution is heated, solvent vapour leaves the solution. It moves away and is cooled and condensed. The remaining solution becomes more concentrated as the amount of solvent in it decreases.

## Slide 4
Developing Experts All rights reserved © 2021
KS4-17-09: Using Resources - Explore water safe to drink
● Describe the difference between potable and pure water
● Describe the steps used to produce potable water from fresh water and from salty water
Extended writing: describe the process of desalination.
______________________________________________________________________________________________________________________________________________________________________
______________________________________________________________________________________________________________________________________________________________________
______________________________________________________________________________________________________________________________________________________________________
______________________________________________________________________________________________________________________________________________________________________
Extended writing: describe the process of distillation
______________________________________________________________________________________________________________________________________________________________________
______________________________________________________________________________________________________________________________________________________________________
______________________________________________________________________________________________________________________________________________________________________
______________________________________________________________________________________________________________________________________________________________________
Extended writing: explain why distillation separates substances.
______________________________________________________________________________________________________________________________________________________________________
______________________________________________________________________________________________________________________________________________________________________
______________________________________________________________________________________________________________________________________________________________________
______________________________________________________________________________________________________________________________________________________________________
Explain what happens to substances during the process of distillation in terms of intermolecular forces of attraction.
______________________________________________________________________________________________________________________________________________________________________
______________________________________________________________________________________________________________________________________________________________________
______________________________________________________________________________________________________________________________________________________________________
______________________________________________________________________________________________________________________________________________________________________
______________________________________________________________________________________________________________________________________________________________________
______________________________________________________________________________________________________________________________________________________________________
______________________________________________________________________________________________________________________________________________________________________
______________________________________________________________________________________________________________________________________________________________________